## Slide 1
Thermogeology and hydrogeology
You don ’ t have to be a hydrogeologist to study thermogeology, but it certainly helps.
A practical hydrogeologist often tries to exploit the earth ’ s store of groundwater by
drilling wells and using some kind of pump to raise the water to the surface where it
can be used. A thermogeologist exploits the earth ’ s heat reservoir by drilling boreholes
and using a ground source heat pump to raise the temperature of the heat to a useful
level. The analogy does not stop here, however. There is a direct mathematical
analogy between groundwater flow and subsurface heat flow.
We all know that water, left to its own devices, fl ows downhill or from areas of high
pressure to low pressure. Strictly speaking, we say that water fl ows from locations of
high head to areas of low head (Box 1.2 ). Head is a mathematical concept which combines
both pressure and elevation into a single value. Similarly, we all know that heat
tends to fl ow from hot objects to cold objects. In fact, a formula, known as Fourier ’ s
law, was named after the French physicist Joseph Fourier. It permits us to quantify
the heat fl ow conducted through a block of a given material (Figure 1.2 ):

## Slide 26
Transient Effects
A number of studies have demonstrated the role of transient geological processes
on crustal temperatures. Large-scale tectonic processes (thrusting events, erosion,
and sedimentation) can result in temperature differences reaching several tens
of degrees centigrade at a few kilometers depth (England and Thompson, 1984;
Ruppel and Hodges, 1994). Magma emplacement or presence of hydrothermal
convection at shallow depths may also explain disturbed temperature profiles
(Cathles, 1977; Norton and Hulen, 2001).
Because thermal diffusivity of rocks is low, transient thermal evolution of
rocks undergoing conducting processes is very slow, and return to equilibrium
temperatures may last several tens to hundreds of million years. Figure 1.6
illustrates some examples of large-scale thermal evolution of the crust undergoing
tectonic events. One may note that in the case of a thrusting event, the equilibrium
thermal field (with amaximum temperature of 820 ◦C) is reached 120 Myr after the
onset of thrusting. On the contrary, when convective processes are involved around intrusive bodies, heat transfer mechanisms through fluid circulation are accelerated, and typical timescales are lower than 1 Myr (Cathles, 1977). When smaller scale systems are considered, thermal equilibrium is reached faster. For example, serpentinization of oceanic crust may result in large amplitude thermal signatures lasting less than a few thousands of years (Emmanuel and Berkowicz, 2006).

## Slide 28
Role of Anisotropy of Thermal Conductivity
Apart from steady-state heat refraction due to thermal conductivity contrasts or
variations in heat production rates, other subtle effects affecting thermal properties
may trigger thermal anomalies. Temperature dependence of thermal conductivity is
one example, as shown in Clauser and Huenges (1995). In the case of sedimentary
basins, porosity dependence of thermal conductivity is also significant, as shown
in several studies (Beziat, Dardaine, and Gabis, 1988; Waples and Tirsgaard, 2002).
Sedimentary basins correspond to interesting geothermal targets all the more
that numerous temperature measurements may be available. When thick clayey formations are present in a basin, the role of compaction has to be accounted
for since porosity decreases with compaction pressure and particles’ orientation
becomes horizontal with increasing pressure (Vasseur, Brigaud, and Demongodin,
1995). Both effects together with temperature-dependence effect induce important
changes in thermal conductivity. First, the decreasing porosity (and thus amount
of water) with depth tends to increase thermal conductivity, while temperature
dependence tends to decrease it (see Harcou‥et et al., 2007 for details). Second,
the horizontal orientation of individual clay particles develops anisotropy, favoring
lateral heat transfer and hindering vertical heat flow.

## Slide 29
An example of the effect of thermal conductivity anisotropy on thermal field is
illustrated in Figure 1.7, where the Paris basin is modeled according to Demongodin
et al. study (1991)). Anisotropy ratio is increased with depth and thermal boundary
conditions enable to reproduce measured surface heat flow values. Figure 1.8b
shows horizontal temperature profiles at 1500mdepth, with and without anisotropy
effect. When anisotropy is accounted for, heat accumulates more efficiently within
the basin and a 20 ◦C difference with the isotropic case is reached at basin
boundaries. Obviously, the importance of the anomaly critically depends on thermal
conductivity values and anisotropy ratios. Measurements on representative core
samples, and scaling with in situ conditions are thus of major importance when
thermal modeling of a sedimentary basin is performed (Gallagher et al., 1997).