## Slide 1
A cubic batolite of granite, with a thermal conductivity of 3.1 W/m K,
the side of the cube is 1.5 km and it is placed between two boundary layers.
The upper layer is at 80 ° C, while the bottom layer is at 100 ° C.
What is the flow of heat through the core of rock?
80 ° C
100 ° C
3.1 W/m K

## Slide 2
100 ° mV/mq
Calculate the thermal conductity for each layer

## Slide 3
Problem 1
Let us return to our example, with a diffusivity of 7 × 10 − 7 m 2 s − 1 . During a warm day (12 h = 43 200 s), one might expect a pulse of heat (diurnal temperature signal) to penetrate XXXX???.
Problem 2
During a summer (182 day = 1.57 × 10 7 s), one might expect a pulse of heat (seasonal temperature signal) to penetrate xxxxxx?

## Slide 4: Geothermics 2025-2026 Geothermal energy: a picture into the World

## Slide 5: Net production by technology (GWh)
Geo
Hydro
Wind
Biomass
Solar
Hydro
Geo
Wind
Solar
Other

## Slide 16
Radioactivity as an omnipresent natural phenomenon
element | mean content in the earth‘s crust | mean heat production [µW/t]
U | 2,5 ppm | 0,24
Th | 10,3 ppm | 0,26
K | 2,87 % | 0,09
Σ |  | 0,60
Occurrence of „primordial“ radionuclides (existing since formation of elements) :
Uranium: 238U - 4,5 · 109 y, decay chain, 1 ppm ≙ 12,4 Bq/kg
235U - 0,7 · 109 y, decay chain, 1 ppm ≙ 0,57 Bq/kg
Thorium: 232Th - 1,4 · 1010 y, decay chain, 1 ppm ≙ 4,07 Bq/kg
Potassium: 40K - 1,2 · 109 y, 1 % ≙ 306 Bq/kg
total heat production:
Radioactivity (crust):
≈ 0.9 ∙ 1021 J/ y
Gravitation (mantle, core):
≈ 0.3 ∙ 1021 J/ y
Stober, I., Bucher, K.: Geothermie, Springer Berlin Heidelberg 2012
 Geothermal energy is a “green nuclear power”
What is Geothermal Energy?

## Slide 21
In a geothermal system the meteoric waters are trapped in the reservoir, are heated and it is activated a natural convective circulation, driving the heat up to the surface.
It is necessary the presence of an heat source nearby the surface.
Heat Source
It is necessary to have a reservoir, i.e. a porous and fractured rock system, where there are fluids (water or steam), which can be used as carrier of the heat
Heat Source
Reservoir
It is necessary to have an impermeable coverage, for keeping the fluid and the heat in a confined space.
Heat Source
Reservoir
Coverage
What is Geothermal Energy?

## Slide 22
Heat source
Impermeable basement
Reservoir:
fluid inside a porous and permeable rock)
Impermeable coverage
STEAM
What is Geothermal Energy?

## Slide 23
What is Geothermal Energy?

## Slide 24
Geyser - Iceland
Boiling spring - USA
What is Geothermal Energy?

## Slide 25
Lagoncelli, putizze and old wells San Federico c/o Lago Boracifero
What is Geothermal Energy?
“Bocca della Balena” (Whale Mouth) Bagni San Filippo

## Slide 26
Mud Lagoncelli
Sant’Adriana
Geothermal manifestation Monterotondo Marittimo
What is Geothermal Energy?

## Slide 27
Champagne pool – New Zealand
What is Geothermal Energy?

## Slide 28
The World Geothermal Electricity Status
27
12,6 GW

## Slide 29
The World Geothermal Electricity Trend
28
0
5.000
10.000
15.000
20.000
25.000
1995
2000
2005
2010
2015
2020
6.832
7.973
8.903
10.897
12.635
21.443
MW
Years
World Geothermal Electricity

## Slide 30
The global project pipeline totals 20 GW across all development stages
The World Geothermal Electricity Trend

## Slide 31
COUNTRY | 2010 MW | 2010 GWh | 2015 MW | 2015 GWh
USA | 3,093 | 16,603 | 3,450 | 16,600
PHILIPPINES | 1,904 | 10,311 | 1,870 | 9,646
INDONESIA | 1,197 | 9,600 | 1,340 | 9,600
MEXICO | 958 | 7,047 | 1,017 | 6,071
NEW ZEALAND | 628 | 4,055 | 1,005 | 7,000
Top 5 Countries: installed capacity>1 GW
30
Notes: 30

## Slide 32
COUNTRY | 2015MW | 2015 GWh | NEW MW | NEW GWh
KENYA | 594 | 2,848 | 392 | 1.418
USA | 3,450 | 16,600 | 352 | 
TURKEY | 397 | 3,127 | 306 | 2.637
NEW ZEALAND | 1,005 | 7,000 | 243 | 2.945
INDONESIA | 1,340 | 9,600 | 143 | 
31
Top 5 Countries: incremental capacity>100 MW
Notes: 31

## Slide 33
32
Kenya
Ten new Units for 390 MW at Olkaria, which is approaching to the 600 MW threshold. The other geothermal area of the country is Eburro, still at initial development phase.
Notes: 32

## Slide 34
33
USA
New Units in California, Hawaii, Nevada, New Mexico, Utah and Wyoming.
Notes: 33

## Slide 35
34
Turkey
14 new Units for about 300 MW, located mainly in western Anatolia, on Menderes, Gediz and Simav valleys; a small unit in Çanakkale
Notes: 34

## Slide 36
35
New Zealand
About 250 new MW from 8 units at Ngatamariki, Tauhara and Wairakei. All the fields are in central part of North island, except Ngawha.
Triple Flash, Fuji, 132 MW, Nga Awa Purua, Rotokawa
Notes: 35

## Slide 37
36
Indonesia
New plants have been commissioned at Flores – Ulumbu and Mataloko, Sulawesi – Lahendong and Sumatra - Ulu Belu.
Ulu Belu plant, 2x55 MW, single flash, Toshiba.
Notes: 36

## Slide 38
COUNTRY | 2015MW | 2015 GWh | NEW MW | NEW GWh | % MW | % GWh
TURKEY | 397 | 3,127 | 306 | 2.637 | 336% | 539%
GERMANY | 27 | 35 | 20 |  | 280% | 
KENYA | 594 | 2,848 | 392 | 1.418 | 194% | 99%
NICARAGUA | 159 | 492 | 72 | 182 | 82% | 59%
NEW ZEALAND | 1,005 | 7,000 | 243 | 2.945 | 32% | 73%
37
Top 5 Countries: incremental capacity>30%
Notes: 37

## Slide 39
38
Germany
Fuor new binary units about 5 MW each and district heating at Sauerlach,
Dürrnhaar,
Kirchstockach
and Insheim
Notes: 38

## Slide 40
39
Nicaragua
New units at San Jacinto-Tizate 2x26 MW Fuji single flash
Notes: 39

## Slide 41
3rd
Top Dozen of Geothermal Fields
The Geysers, 1°
California, USA
1585 MW
Cerro Prieto, 2°
México
727 MW
Larderello, 4°
Italy
595 MW
Salak 9°
Indonesia
377 MW
Salton Sea, 8°
California, USA
388 MW
Coso, 11°
California, USA
292 MW
Mak -Ban 6°
Philippines
458 MW
Darajat 12°
Indonesia
260 MW
Hellisheidi, 10°
Iceland
303 MW
Tongonan 3°
Philippines
726 MW
Wairakei 7°
New Zealand
399 MW
Olkaria, 5°
Kenya
592 MW
1st
2nd
4th
5th
40
Notes: 40

## Slide 42
41
Iceland
New units in Hellisheidi 2x45 MW single flash Mitsubishi;
Focus on heating and cascade applications.
Notes: 41

## Slide 43
A new unit in Bagnore (40 MW);
the first italian binary unit; the first hybrid projet geothermal-biomasses.
42
Italy
90 MW in a snapshot: Carboli, San Martino & Monte Rotondo
Notes: 42

## Slide 44
Larderello: the birthplace of geothermal industry
The Devil Valley in Larderello
No exploration activity needed……
Before the beginning…
43

## Slide 45
1904: first experiment
1913: first 250 kW unit
Larderello: the birthplace of geothermal industry
The initial steps…
44

## Slide 46
The pioneering stage
45

## Slide 47
1900
1950
1955
1960
1965
1970
1975
1980
1985
1990
1995
2000
2005
2011
The history
Natural manifestations areas
New production record in 2011: 5315 GWh
Reaching the field boundaries
46

## Slide 48: Production sustainability Deep exploration
Temperature at 3000 m b.g.l.
Temperature at the top of the
shallow Carbonate Reservoir
W
W
E
A unique system at great depth
47

## Slide 49
Geothermal power generation in Italy
Where and its characteristics
48
Larderello
since 1913
250 km2
more than 200 wells (production + reinjection)
superheated steam (2-18 bar & 150-270°C)
depth: 200 m – 2000 m
Radicondoli
since 1950
50 km2
about 30 wells (production + reinjection)
superheated steam (8-20 bar & 190-250°C)
depth: 800 m – 4000 m
Mt. Amiata
since 1955
30 km2
about 40 wells (production + reinjection)
liquid dominated (300-350°C)
depth: 2000 m – 4500 m
Currently Enel Green Power is the only that produces electricity from geothermal sources in Italy.

## Slide 50
Deep drilling
Technological improvements were required
High temperature logging tools
New exploration techniques
Fluid treatment
49

## Slide 51: Production sustainability Reinjection in the Valle Secolo area
Reinjection represents by now an “exploitation strategy”
50

## Slide 52: Production sustainability Power plants efficiency improvement
12 new units (314,5 MW) were installed and started up in the period 2000-2023 in the area of Larderello-Travale/Radicondoli
8 units, for a total of 214.5 MW, replaced old units in operation from many years and considered “obsolete”. The new units are characterized by higher efficiency and lower environmental impact.
4 units, for a total of 100 MW are new capacity installed both in marginal and central areas
37 new units with a capacity in the range 8 - 60 MW have been started up in the Larderello-Travale area in the period 1980 -2023
51

## Slide 53
Design and construction of a specific plant, know as AMIS© (Abbattimento Mercurio e Idrogeno Solforato) for the abatement of H2S (hydrogen sulphide) and Hg (mercury) from the gases emitted during power plants operation
Environmental sustainability
Innovation also possible to reduce environmental impact
New design solution and criteria for minimizing visual impact of the power plants in order to make geothermal presence more acceptable to the local community
Plant design innovation
Architectural innovation
52

## Slide 54
Reduction of gas emission AMIS (process for H2S and Hg removal)
  Abatement
  Hg >90%
  H2S 70-80%
New design criteria finalized to minimize the visual impact
Environmental Sustainability
53

## Slide 55: AMIS plants
Some pictures
54

## Slide 56: Steam gathering systems
  Construction at minimal height above ground level and/or in trenches, along roads or woods
  External color blends with landscape
55

## Slide 57: Power plants
  External color blends with landscape
  Architectural elements
56

## Slide 58
Direct use promotion
37% of the heat is delivered to greenhouses
57

## Slide 59
61 district heating networks, using 54% of the total heat dispatched from EGP
Direct use
District heating in Tuscany
58

## Slide 60
Global Geothermal Power Market
Key Barriers and Actions Needed
Resource
Envi ronment
Economics
Social
Demand
GEOTHERMAL EXPONENTIAL GROWTH
Opportuni ty
Barrier | Description | Actions Needed
Resource | Geothermal resource availability Well productivity & field capacity Presence of earthquakes-volcanic activity near the resource | R&D activity: technology improvements to identify the resource and to exploit geothermal resources at different temperatures Coordination of activities to share exploration results (i.e. public databases providing location of resources)
Environment | Regulation for construction and operations Air emissions & noise pollution Visual impact | Coordination of activities to address permitting issues Technological solutions (i.e. Enel development of AMIS technology) Architecture solutions
Project economics | High initial investment costs High O&M costs Financial support and incentives | Coordination at EU, national and regional levels to support and regulate the sector, providing visibility Support bank financing
Social | Misleading information Lack of knowledge Local hostile institutions / environmental associations | Creation of consensus through information and communication Improvement of the relationship with communities
Demand | Trend of energy demand Competition from other renewable sources | Planning of geothermal projects with grid access Support to distributed generation/smart grids
59

## Slide 61
Conventional
Past 5-10 years
Medium term outlook 5-10 years
Long-term outlook 10+ years
Binary cycle
EGS (Pilot project in France)
Today
  Mostly proven and cost-effective technologies
  Incremental plant technological advances going forward
  Binary only as an ancillary application due to infancy stage of technological development (i.e., higher costs)
  Binary proven to be a self-standing technology, increasing overall installable potential
  Economics not yet in line with steam technologies (dry and flash), expected to improve in the long term
  Technology still in “development” phase
  Under certain technological development outlook (i.e., fast decrease in technology costs), expected to increase installable potential
  Cascade utilization are already present in the market
Binary cycle (~1,7 GW of capacity today)
  Dry steam (~3 GW of capacity today)
  Flash steam (~8,4 GW of capacity today)
10
Breakthrough
Geothermal technologies
Past, present and future
Supercritical Fluid (Pilot project in Iceland, Italy, Japan)
Hybridization; Cascade utilization
Cascade utilization
60

## Slide 62: Is it possible a second exponential growth?
Binary plants
Geothermal binary power plant
61

## Slide 63
Binary plants
The Mt. Amiata geothermal field is characterized by a deep water dominated reservoir, at very high temperature >300°C.
The fluid is separated at 20 bar, water at 210°C is reinjected and steam is used for power production.
There are available 250 t/h of 160°C hot water. The presence of silica does not allow the direct utilization of the water, but it is possible to have a second flash at 5 bar, producing 20-30 t/h of steam at 160°C; half of this steam is used in a 1 MW binary plant.
The system is connected with the 20 MW Bagnore 3 plant, and it is even more complex for the presence of a geothermal heating station.
Is it possible a second exponential growth?
62

## Slide 64
Binary plants
Turbine
Heat Exchanger
Is it possible a second exponential growth?
63

## Slide 65: Is it possible a second exponential growth?
Binary plants
Experimental campaign – ORC power plant prototype realization
COD 20-3-2012
Calibration and initial performance tests
August: final set up with improvement in heat exchangers
Long run test
Performance tuning with manufacturer
Preliminary results are promising
64

## Slide 66: Is it possible a second exponential growth?
EGS plants
1.5 + 4.5 MWe
geophone
geophone
production
50 kg/s
production
50 kg/s
600 m
200oC
depth 5000 m
600 m
GPK2
(existing)
GPK3
(existing)
GPK4
(drill 2003)
Observation well
Observation well
Injection
100 kg/s
1400 m
Enhanced Geothermal System: European Soultz project
65

## Slide 67: Is it possible a second exponential growth?
Hybrid plants
Stillwater Solar Geothermal Hybrid Project
World’s first solar/geothermal hybrid project combines the continuous generation capacity of the medium enthalpy geothermal binary cycle with the peak capacity of solar power thus allowing for synergies to be explored.
Integrates 26 MW of solar photovoltaic capacity to EGPNA’s operating 33 MW Stillwater Geothermal Project
Consists of over 89,000 polycrystalline silicon PV panels built on 240 acres. It will generate enough energy to meet the needs of 16,000 American households.
In 2012, this state-of-the art plant won EGPNA the Geothermal Energy Association Honor Award for Technology Advancement which recognizes companies that develop innovative or pioneering technology to further geothermal development.
66

## Slide 68: Is it possible a second exponential growth?
Hybrid plants
Stillwater Solar Geothermal Hybrid Project
67

## Slide 69: Is it possible a second exponential growth?
Stillwater Solar Geothermal Hybrid Project
2009 – began w/ nominal capacity 33.1 MW.
2012 – 26 MW of photovoltaic capacity added.
Production impaired during warm weather, because of dry cooling.
Geothermal brine temperature lower than design, so power island underutilized.
Integration with CSP designed to increase the power output.
68
Hybrid plants

## Slide 70: Is it possible a second exponential growth?
Stillwater Solar Geothermal Hybrid Project
2009 – began w/ nominal capacity 33.1 MW.
2012 – 26 MW of photovoltaic capacity added.
Production impaired during warm weather, because of dry cooling.
Geothermal brine temperature lower than design, so power island underutilized.
Integration with CSP designed to increase the power output.
17 MWth
24,000 m2 of parabolic trough collectors
11 parallel loops
Heat Transfer Fluid (HTF) is demineralized water with a corrosion inhibitor added
Solar inlet temperature – 300°F/149°C
Solar outlet temperature - 390°F/ 199°C
Hybrid plants
69

## Slide 71: Is it possible a second exponential growth?
STEAM FROM THE WELLS
BIOMASS
BOILER
GEO PLANT
Site | Technology | Biomass type | Biomass need [kt/y] | Capacity [MWe]
Cornia 2 | Geothermal steam superheater with biomass firing by combustion grate | Forest & agricultural residues, power crops | 43 | 4.8
Hybrid plants
70

## Slide 72: Is it possible a second exponential growth?
Cogeneration plants
 According to heat demand the geothermal water mass flow is splitted
 District Heating system
71

## Slide 74: Is it possible a second exponential growth?
Cogeneration plants
 Cascade Utilizations
73

## Slide 75: Is it possible a second exponential growth?
Cogeneration plants
Production well
Reinjection well
200 - 220 °C
80%
steam
water
20%
40 °C water
30 °C water
 Agricultural Applications
74

## Slide 76: Is it possible a second exponential growth?
Unconventional plants
Conceptual model
of a geothermal
reservoir at
Supercritical Conditions
3,5 km
Minimum Casing depth
4 - 5 km
Target depth
75

## Slide 77: Sustainable Development
76

## Slide 78: Sustainable Development
Natural (&reinjected) fluid recharge
Exploitation
Thermal Flux
77

## Slide 79: Sustainable Development
A block of rock is by no means compact and waterproof, as it seems:
thanks to empty spaces (pores) and capacities (which cause permeability)
it is able to circulate water and keep a certain amount of it inside.
78

## Slide 80: Sustainable Development
The earth's heat flux of 300 mW/m2 behaves like hot coals under a grill: the meat cooks because it absorbs the heat that comes from the coals.
79

## Slide 81: Sustainable Development
Schematizing a block of underground rock measuring 100x100x500 meters,
with the terrestrial heat flow that passes through it from bottom to top,
and by circulating 10 kg/s of water, a warming, even if modest, is observed
100x500 (m2)x0,3 (W/m2) / 4186 (J/kg °C)x10 (kg/s)= delta T = 0,4°C
Water inlet
Water outlet
“heated”
80
earth's heat flux of 300 mW/m2

## Slide 82: Sustainable Development
81

## Slide 83: Sustainable Development
But if I imagine that our rock has been exposed to heat flow for a "geological" time, it behaves like a soapstone, that is, it cooks the meat by virtue of the heat stored in it, and not the dynamic flow, which we have seen to be negligible
The geological time required to heat the given volume of rock by 200 ° C with the geothermal flow amounts to about 5000 years
82

## Slide 84: Sustainable Development
A productive well, without reinjection, progressively empties the system of water stored in the pores
83

## Slide 85: Sustainable Development
I therefore produce with a declining flow rate, at a constant temperature, emptying the water contained within the rock
Chart: Time [years]
84

## Slide 86: Sustainable Development
A productive well and a reinjection well, using water as a medium of exchange to remove the heat contained in the rock
85

## Slide 87: Sustainable Development
It is therefore possible to obtain a more effective exploitation…
86

## Slide 88
.. which progressively removes the heat that had accumulated in the soapstone, but still allowed us a sumptuous banquet!!
87
Sustainable Development

## Slide 89
A new model of approach is possible, based on the concept of agricultural rotation: I alternately exploit different areas of a larger area, keeping the others at rest, and allowing them to be recovered in terms of nutrients.
88
Sustainable Development

## Slide 90
.. I therefore hypothesize a more complex system, with four groups of production-reinjection wells, over a large area, with rotation exploitation of 50 years, I can reach a sustainable development approach, constantly extracting 150 MW of electricity from an area of ​​15x15 km2…
89
Sustainable Development

## Slide 91: Sustainable Development
..with an almost total rebalancing of the temperature in the waiting phase between one cycle and another, for each cultivation pole, due to the thermal flow (over an area 4 times greater than that in which they are exploited from time to time) and the circulation of water which, through convective motions, homogenizes the temperature in the entire volume.
90

## Slide 92
Geothermal Energy:
FIRE
WITHOUT
SMOKE
Geothermal advantages
91