## Slide 1
0 - 500 m
500 – 5000 m
More than
5000 m
Mostly for Direct uses of heat
Borehole Heat Exchanger
Power generation – Heat&Power generation
Conventional technologies –
EGS (Engineered Geothermal Systems)
EGS – Supercritical fluids
Future perspectives
Dry/hydrothermal
Shallow Reservoir
Hydrothermal Systems: shallow and deep reservoir
Hot deep dry/wet rock
reservoir
Depth
Depending on the depth and the physical properties of the resource, the heat&power production, the upfront cost and the appropriate utilization technology may vary.
Geothermal Energy: actual technology and future perspective

## Slide 2: Electricity production
Groundwater heat is not used directly for energy production, but through a mass of water that exchanges and extracts the heat stored in the rocks (hydrothermal systems)
Electrical power is produced by the conversion of thermal energy stored in the mass of water (T from 90°C to 350°C) into mechanical energy through a turbine, either directly (conventional flash technology) or indirectly (binary technology), and finally in electricity thanks to the generator

## Slide 4
Steam dominant systems: liquid water and steam normally coexist in the tank, which is the continuous phase that controls the pressure. They are high temperature systems and normally produce dry or superheated steam. Geothermal systems of this type are very rare (Larderello in Italy, The Geysers in California, Matsukawa in Japan, Kamojang and Darajat in Indonesia).
Water-dominant systems: Liquid water is the continuous phase, which controls the pressure. Steam may be present, in the form of bubbles. These geothermal systems (125°C < 225°C) are the most widespread in the world. They can produce, depending on their temperature and pressure, hot water, a mixture of water and steam, wet steam and, in some cases, dry steam. They are the most widespread (e.g. Wairakei in New Zealand, Tongonan in the Philippines, and Cerro Prieto in Mexico).

## Slide 5
Dry steam systems
Vapor separation systems (single or double flash)
Binary plant
hybrid plants
WATER VAPOUR SYSTEMS
Dominant water systems
Electricity production

## Slide 10
The production of electricity from conventional geothermal plants consists of the conversion of heat from medium and high temperature aquifers (from 90°C to 350°C) through the use of turbogenerators.
10 MWt (heat) 1MWe (power)
1 MWe needs:
7 - 10 t/h dry vapour
30-40 t/h of two-phase fluid at 200-250°C (flash technology)
400 - 600 t/h of water if using low-enthalpy ORC binary cycles (120-160°C)
Power production

## Slide 11
Mondo
da Bertani, 2013

## Slide 12: UNCONVENTIONAL GEOTHERMAL SYSTEMS
There are not only hydrothermal systems and geoexchange probes
New technologies for the use of unconventional geothermal resources
(UGR=Unconventional Geothermal Systems)

## Slide 13: Hot brine systems
They are particular types of hydrothermal system, in which, due to the peculiar genetic characteristics of the water originally present in the system,
- lateral sealing of the reservoir due to different hydrogeological conditions and/or due to hydrothermal encrustations,
poor recharge with "fresh" rainwater, and above all due to a prolonged convective circulation driven by strong values of the geothermal gradient in a closed environment at high temperature,
the original waters have undergone a long process of salt concentration, reaching the levels of a real brine (total TDS >> 100 mg/l).
These are systems whose fluids, if on the one hand to be used for geothermal purposes require elaborate and expensive chemical treatments and special generation plants, on the other hand have the advantage of being able to produce valuable mineral compounds CRITICAL ROW MATERIALS.

## Slide 14: Geopressurized Systems
Clastic complexes with sand grain size, rather young (<10 Ma) and therefore not yet diagenized, very permeable due to primary porosity, forming aquifers confined to depths > 2km,
in which the water pressure is regulated not by the hydrostatic load but by the lithostatic of the overlying formations (and also lateral ones in compression regime).
The pressure of the fluids in the aquifer can reach several hundred atmospheres.
The systems form in areas of weak thermal anomaly, the temperature of the water in the reservoir varies with depth as a function of normal or slightly anomalous values ​​of the geothermal gradient.
Dissolved in water there are almost always significant quantities of organic gases, which may have commercial interest and which enhance the economic value of extractable geothermal heat (tri-generation).

## Slide 15: Magmatic resources
Systems connected to active volcanic apparatuses with a magma chamber at a shallow depth (< 5-6 km), in which the temperature of the fluid used for heat extraction depends on that at the roof of the igneous body.
Different methods of heat capture have been devised for this purpose, but have not yet been tested.
The main of these methods are:
to circulate water with reverse circulation in wells of large diameter with bottom scarp a few tens of meters from the roof of the magma chamber, equipped with ascent tubing inside an injection casing;
fracture the vitrified Cap Rock to the roof of the magma chamber by drilling pairs of injection and production wells, to circulate surface water in a closed loop in the artificial reservoir created in the Cap Rock itself.

## Slide 16: Supercritical fluid systems
The fluids contained in the tank (located at considerable depths and sealed to the roof by an efficient covering blanket) are formed under very high temperature and pressure conditions.
Therefore, they possess an energy density much higher than that of fluids extractable from high-temperature hydrothermal systems, even those with dominant steam.
High-temperature hydrothermal systems, both water and steam-dominant, are likely to evaporate at depth into reservoirs containing supercritical fluids.
It is probable that in the most thermally anomalous areas the fluids contain aggressive compounds due to F and Cl acids.

## Slide 17: Engineered Geothermal Systems)
EGS= Enhanced/Engineered Geothermal Systems
In these systems, the reservoir is created in whole or in part artificially by hydrofracturing operations and/or by chemical means. The heat contained in the rocks and fluids that permeate the pores and fractures (natural or newly formed) of the reservoir rocks is partially removed and transferred to the surface by means of closed-circuit water circulation, introduced from the outside with injection wells and extracted with production wells.

## Slide 18: EGS (Engineered Geothermal Systems)
Fluid
Serbatoi idrotermali
Enhanced Geothermal System (EGS)
Temperature
Permeability

## Slide 19: Injection well in rock with low permeability and sufficient T°
Come funziona
Enough P-water is injected to fracture or widen existing fractures
Hydrofracturing continues to extend the fractures
Through the production well that intercepts the fractures, the water is circulated and heated
Production through new wells and extensive fracturing/circulation

## Slide 20: EGS, HDR, HWR, HFR
Many acronyms have been coined over time
HDR Hot Dry Rocks (the first concepts and experiments in the USA, UK, Japan and France)
HWR Hot Wet Rocks
HFR Hot Fractured Rocks
Today experimentation has demonstrated the difficulty of fracturing "dry" rock, and the effectiveness of operating in already fractured rocks, to stimulate natural fracturing perhaps reduced by self-sealing or other processes (to be studied)
Current projects, in France, Australia and the USA they are dedicated to EGS, a term still under discussion but which essentially indicates the artificial increase of permeability in reservoir rocks.
Advantages of EGS: they can be calibrated to ensure sustainable use of the resource, using production systems capable of sustaining production levels over long periods of time.
The longevity of production can be ensured by using moderate production levels, which take into account the local characteristics of the resource.

## Slide 21: UGR systems
The extension of geothermal resources beyond their conventional use requires the development of new methods that allow for the exploration, development and exploitation of those resources that are not economically accessible with conventional methodologies.
The ultimate goal is to develop a technology capable of producing electricity and/or heat by exploiting a de facto ubiquitous resource – heat within our planet – in ways that are economically accessible and environmentally friendly. at the same time relatively independent of the specific characteristics of the site.
exploration
resource evaluation
resource management
advanced drilling
advanced stimulation
efficient power cycles
environmental impact

## Slide 22: EGS
EGS systems can be calibrated to ensure sustainable use of the resource, using production systems capable of sustaining production levels for long periods of time.
Longevity of production can be ensured by using moderate production levels, which take into account the local characteristics of the resource.

## Slide 23: EGS
With a large flow rate (500 l/s), production starts with a capacity of 45 MWe but ends after 20 years; Total generation is 245 MWeyear.(from Sanyal & Butler 2005)

## Slide 24: EGS
A lower flow rate (126 l/s) is sustainable and long-lasting: the total generation is comparable to the previous case (250 Mwe per year)(from Sanyal & Butler 2005)

## Slide 25
Concetto
Pozzo esplorativo
Sviluppo
Produzione
Ripristino
Scelta sito
Dimostrazione Fattibilità
Approntamento impianti
Raggiungimento fine produzione
Pianificazione e celta della zona migliore su basi:
Concettuali
Tecniche
Politiche e ambientali
Economiche
Pozzo pilota
Test idraulici
Produzione
Modellistica di serbatoio
Pozzi produzione e reiniezione
Test produzione
Installazione impianti
Produzione elettricità e/o calore
Gestione
Reinvestimento sito o smantellamento
?
Esplorazione
Perforazione, sviluppo del campo
Coltivazione
e rischi legati alle varie fasi di vita di un progetto

## Slide 26
Ultimate goals of R&I
Increase exploitable volumes
Reduce risk of not finding permeability
Reduce costs

## Slide 27
Geothermal Electricity: new technology
and research efforts
Exploration and investigation technology: Improvement of the probability of finding an unknown geothermal reservoir and better characterize known reservoir, optimizing exploration and modeling of the underground prior to drill. Require also clear terminology, methodology and guidelines for the assessment of geothermal potential. It will result in an increased success rate.
Drilling technology: improvements on conventional approaches to drilling such as more robust drill bits, innovative casing methods, better cementing techniques for high temperature, improved sensors, electronic capable of operating at higher temperature in downhole tools, revolutionary improvements utilizing new methods of rock penetration. It will result in reducing the drilling cost and it will allow to access deep and hot regions.
Power conversion technology: improving heat-transfer performance for low temperature fluid, developing plant design with high efficiency and low parasitic losses. It will increase the available resource basis to the huge low-temperature regions, not only those having favorable geological conditions.

## Slide 28
Operation technology: increasing production flow rate by targeting specific zones for stimulation, improving heat-removal efficiency in fractured rock system. Refine stimulation methods (permeability enhancement) for Engineered Geothermal Systems (EGS) and reduce the risk associated with induced seismicity. It will lead to an immediate cost reduction increasing the output per well and extending reservoir operating life.
Unconventional Geothermal Systems (UGR) technology: emerging activities to harness energy from nowadays non-economic reservoir would make significant progress with qualified input from research. in particular, reservoirs with supercritical fluids (fluids in the thermodynamic area above the critical temperature and pressure) and geopressurized reservoirs (deep sedimentary basins where fluids show high pressure and are rich of chemical elements or gases). This includes, beside peculiar power conversion and reservoir technology, also Operation & Maintenance techniques in aggressive geothermal environments, since they require specific solutions for corrosion and scaling problems. It will lead to an overall increase in power production
Geothermal Electricity: new technology
and research efforts

## Slide 29
Management technology: retrieve, simulate and monitor geothermally relevant reservoir parameters that influence the potential performance and long-term behavior. It includes the development of a Zero-emission technology, by mean of the total reinjection of fluid (and gases) within the reservoir without cooling and secondary effects It will secure the sustainable production achieved by using the correct production rates, taking into account the local resource characteristics (field size, natural recharge rate, etc.), extending the reservoir operating life and producing a benefit for the environment.
Geothermal Electricity: new technology
and research efforts

## Slide 30: JOINT PROGRAMME on GEOTHERMAL ENERGY
The goal of the JPGE is to contribute to the achievement of the SET Plan objectives, streamlining and coordinating national R&D programmes, accelerating the targeted development and maturing of next generation geothermal technology in order to provide industry with all the elements required for its large-scale and cost-effective deployment.
This target can be reached only through the application of new cost-effective technologies able to enhance the production of the already identified resources, to discover new untapped hydrothermal systems and to develop non hydrothermal systems.

## Slide 31
The GEISER (Geothermal Engineering Integrating Mitigation of Induced Seismicity in Reservoirs) project started at the beginning of the year 2010, with a funding of € 5.3 Mio granted for 3.5 years
Goal: to develop strategies to fulfil the task of the stimulation and improve the hydraulic properties of the geothermal reservoir without producing large earthquakes that pose a threat to buildings and disturb the public.
International Projects
Analysis of induced seismicity
Understanding the geomechanics and processes involved in induced seismicity
Consequences of induced seismicity
Strategies for the mitigation of induced seismicity

## Slide 32: The resource assessment in the context of Geo-ELEC
Fitting to the aim of Geo-ELEC
Build resource assessment of Europe for geothermal power
Time horizons of 2020 and beyond
Build on existing methodologies
Proposed assessment methodology
Presentation on pan-european scale (WebGIS with resource potential in map view)
International Projects

## Slide 34
Minimum LCOE nel 2030 in €/MWe

## Slide 35
Valutazioni ambientali, azioni di mitigazione e monitoraggio
VIA: è l’insieme degli effetti diretti o indiretti, positivi o negativi, permanenti o temporanei, singoli e cumulativi indotti sull’ambiente, considerando anche gli impatti socio-economici.
Perforazione e
Test di pozzo
Progettazione e
Costruzione
impianto
Esercizio
Valutazione
della Risorsa
Ripristino
VIA – VALUTAZIONE DI IMPATTO AMBIENTALE

## Slide 36
L’energia geotermica fornisce una serie di vantaggi ambientali nei confronti delle fonti fossili in termine di emissioni gassose in quanto la produzione geotermoelettrica non rilascia NOx, SO2 e minor quantità di CO2 rispetto alla produzione di energia elettrica da risorse fossili (carbone, oli combustibili, …).
Mitigazione  sistemi di abbattimento per H2S e Hg, programmi di monitoraggio per le emissioni e per la qualità dell’aria.
EMISSIONI IN ATMOSFERA

## Slide 37
Per la classificazione dei rifiuti non pericolosi e pericolosi si fa riferimento alla normativa comunitaria
RIFIUTI SPECIALI NON PERICOLOSI
Detriti provenienti da perforazioni geotermiche
RIFIUTI SPECIALI PERICOLOSI
Fanghi prodotti nella condensazione del vapore geotermico
Residui di materiali contaminati da fluidi geotermici
Mitigazione  SMALTIMENTO O RECUPERO
RIFIUTI SPECIALI

## Slide 38
Il rumore è prevalentemente connesso a 3 FASI:
PERFORAZIONE
COSTRUZIONE
TURBINE, COMPRESSORI, TORRI DI RAFFREDDAMENTO
L’impianto di produzione in condizioni normali ha un rumore molto ridotto.
Mitigazione  Durante la perforazione uno schermo protettivo temporaneo può essere costruito attorno alla piattaforma di perforazione ed attorno ad alcuni macchinari.
Le costruzioni che contengono i generatori e le turbine sono in genere progettati per garantire un isolamento acustico e termico, attraverso delle pareti insonorizzate.
INQUINAMENTO ACUSTICO