## Slide 1: GEOTHERMAL ENERGY:
PAST, PRESENT and future

## Slide 2: PAst
Natural Heat of the Earth that is derived from the original formation of the planet and from the decay of the radioactive elements in the Earth’s crust.
Creation
Surface evidence of this Heat around the world and over the centuries.
Evidence
Geothermal springs used for heating and cooking. Initial therapeutic applications and use of volcanic stones.
Usage
Thermal Baths. Present in the culture of various peoples of the past and still in those of the present.
Usage
First use of district heating to heat an entire community occurred in Chaudes-Aigues, France, in the 14th Century.
Usage
In the early 20th century first geothermal power plant to produce electricity in Larderello, Italy.
Usage

## Slide 3: LARDERELLO
DRY STEAM POWER PLANT
Geothermal reservoir filled naturally with steam
Steam dominant system
Extraction and Injection wells
Turbine generator
Condenser + Cooling tower
1913: first 250 kW unit.
Now 34 plants, with 37 generating units and a total capacity of about 800 MW.

## Slide 4: Present
Different ways to collect the underground Heat to produce electricity.
An energy-efficient heating and cooling system. Closed loop system.
Geothermal heat is used directly rather than for power generation.
Hot springs for therapeutic use.
Geothermal Power Plants
Heat Pumps
District heating
Thermal Baths

## Slide 5: GEOTHERMAL POWER PLANTS
Flash Steam Power Plant
Binary Cycle Power Plant
Single or double flash
Dominant water system
Low temperature (≈100°)
Geothermal water only used for heating another fluid (iso-butane, iso-pentane)

## Slide 6: GROUND SOURCE HEAT PUMP
Temperature of rocks and soil only a few meters beneath surface constant range from 5 to 10°C
Machine that causes thermal energy to flow up temperature, requires work
Heating/cooling system
Closed loop system

## Slide 7: DISTRICT HEATING
Nesjavellir, ICELAND
Volcanic Iceland, active volcano belt
Generates both electricity and hot water for district heating
Very little thermal energy lost, well insulated pipe ( 25Km far from the capital Reykjavik)
More than 45% of Iceland’s primary energy use comes from geothermal sources
87% of all buildings are heated with geothermal water

## Slide 8: FUTURE
Increase permeability in marginally productive geothermal system.
Unconventional Geothermal System
Enhanced Geothermal System
Magma
Supercritical fluid
Geopressured reservoir

## Slide 9: UNCONVENTIONAL GEOTHERMAL SYSTEMS
There are not only hydrothermal systems and geoexchange probes
New technologies for the use of unconventional geothermal resources
(UGR=Unconventional Geothermal Systems)

## Slide 10: UGR systems
The extension of geothermal resources beyond their conventional use requires the development of new methods that allow for the exploration, development and exploitation of those resources that are not economically accessible with conventional methodologies.
The ultimate goal is to develop a technology capable of producing electricity and/or heat by exploiting a de facto ubiquitous resource – heat within our planet – in ways that are economically accessible and environmentally friendly. at the same time relatively independent of the specific characteristics of the site.
exploration
resource evaluation
resource management
advanced drilling
advanced stimulation
efficient power cycles
environmental impact

## Slide 11: UNCONVENTIONAL GEOTHERMAL SYSTEM
Supercritical fluid
Geopressured reservoir
Thermal energy from Magma
Deep sedimentary basins where fluids show high pressure and are rich of chemical elements or gases
Above critical temperature and pressure
Combine properties of gas and liquid
Highest heat content

## Slide 12: OVERALL INCREASE IN POWER PRODUCTION but IMPROVING OF DRILLING TECNOLOGY, OF OPERATION AND MAINTENANCE TECHNIQUES.

## Slide 13: Hot brine systems
They are particular types of hydrothermal system, in which, due to the peculiar genetic characteristics of the water originally present in the system,
- lateral sealing of the reservoir due to different hydrogeological conditions and/or due to hydrothermal encrustations,
poor recharge with "fresh" rainwater, and above all due to a prolonged convective circulation driven by strong values of the geothermal gradient in a closed environment at high temperature,
the original waters have undergone a long process of salt concentration, reaching the levels of a real brine (total TDS >> 100 mg/l).
These are systems whose fluids, if on the one hand to be used for geothermal purposes require elaborate and expensive chemical treatments and special generation plants, on the other hand have the advantage of being able to produce valuable mineral compounds CRITICAL ROW MATERIALS.

## Slide 14: Geopressurized Systems
Clastic complexes with sand grain size, rather young (<10 Ma) and therefore not yet diagenized, very permeable due to primary porosity, forming aquifers confined to depths > 2km,
in which the water pressure is regulated not by the hydrostatic load but by the lithostatic of the overlying formations (and also lateral ones in compression regime).
The pressure of the fluids in the aquifer can reach several hundred atmospheres.
The systems form in areas of weak thermal anomaly, the temperature of the water in the reservoir varies with depth as a function of normal or slightly anomalous values ​​of the geothermal gradient.
Dissolved in water there are almost always significant quantities of organic gases, which may have commercial interest and which enhance the economic value of extractable geothermal heat (tri-generation).

## Slide 15: Magmatic resources
Systems connected to active volcanic apparatuses with a magma chamber at a shallow depth (< 5-6 km), in which the temperature of the fluid used for heat extraction depends on that at the roof of the igneous body.
Different methods of heat capture have been devised for this purpose, but have not yet been tested.
The main of these methods are:
to circulate water with reverse circulation in wells of large diameter with bottom scarp a few tens of meters from the roof of the magma chamber, equipped with ascent tubing inside an injection casing;
fracture the vitrified Cap Rock to the roof of the magma chamber by drilling pairs of injection and production wells, to circulate surface water in a closed loop in the artificial reservoir created in the Cap Rock itself.

## Slide 16: Supercritical fluid systems
The fluids contained in the tank (located at considerable depths and sealed to the roof by an efficient covering blanket) are formed under very high temperature and pressure conditions.
Therefore, they possess an energy density much higher than that of fluids extractable from high-temperature hydrothermal systems, even those with dominant steam.
High-temperature hydrothermal systems, both water and steam-dominant, are likely to evaporate at depth into reservoirs containing supercritical fluids.
It is probable that in the most thermally anomalous areas the fluids contain aggressive compounds due to F and Cl acids.

## Slide 17: EGS, HDR, HWR, HFR
Many acronyms have been coined over time
HDR Hot Dry Rocks (the first concepts and experiments in the USA, UK, Japan and France)
HWR Hot Wet Rocks
HFR Hot Fractured Rocks
Today experimentation has demonstrated the difficulty of fracturing "dry" rock, and the effectiveness of operating in already fractured rocks, to stimulate natural fracturing perhaps reduced by self-sealing or other processes (to be studied)
Current projects, in France, Australia and the USA they are dedicated to EGS, a term still under discussion but which essentially indicates the artificial increase of permeability in reservoir rocks.
Advantages of EGS: they can be calibrated to ensure sustainable use of the resource, using production systems capable of sustaining production levels over long periods of time.
The longevity of production can be ensured by using moderate production levels, which take into account the local characteristics of the resource.

## Slide 18: Engineered Geothermal Systems)
EGS= Enhanced/Engineered Geothermal Systems
In these systems, the reservoir is created in whole or in part artificially by hydrofracturing operations and/or by chemical means. The heat contained in the rocks and fluids that permeate the pores and fractures (natural or newly formed) of the reservoir rocks is partially removed and transferred to the surface by means of closed-circuit water circulation, introduced from the outside with injection wells and extracted with production wells.

## Slide 19: ENHANCED GEOTHERMAL SYSTEM
Increase permeability in marginally productive natural hydrothermal systems.
Reservoir is created in whole or in part artificially by hydrofracturing operations and/or by chemical means.
Natural permeability

## Slide 20: EGS (Engineered Geothermal Systems)
Fluid
Hydrothermal reservois
Enhanced Geothermal System (EGS)
Temperature
Permeability

## Slide 21: Injection well in rock with low permeability and sufficient T°
Come funziona
Enough P-water is injected to fracture or widen existing fractures
Hydrofracturing continues to extend the fractures
Through the production well that intercepts the fractures, the water is circulated and heated
Production through new wells and extensive fracturing/circulation

## Slide 22: EGS
EGS systems can be calibrated to ensure sustainable use of the resource, using production systems capable of sustaining production levels for long periods of time.
Longevity of production can be ensured by using moderate production levels, which take into account the local characteristics of the resource.

## Slide 23: EGS
With a large flow rate (500 l/s), production starts with a capacity of 45 MWe but ends after 20 years; Total generation is 245 MWeyear.(from Sanyal & Butler 2005)

## Slide 24: EGS
A lower flow rate (126 l/s) is sustainable and long-lasting: the total generation is comparable to the previous case (250 Mwe per year)(from Sanyal & Butler 2005)

## Slide 25
Ultimate goals of R&I
Increase exploitable volumes
Reduce risk of not finding permeability
Reduce costs

## Slide 26
Geothermal Electricity: new technology and research efforts
Exploration and investigation technology: Improvement of the probability of finding an unknown geothermal reservoir and better characterize known reservoir, optimizing exploration and modeling of the underground prior to drill. Require also clear terminology, methodology and guidelines for the assessment of geothermal potential. It will result in an increased success rate.
Drilling technology: improvements on conventional approaches to drilling such as more robust drill bits, innovative casing methods, better cementing techniques for high temperature, improved sensors, electronic capable of operating at higher temperature in downhole tools, revolutionary improvements utilizing new methods of rock penetration. It will result in reducing the drilling cost and it will allow to access deep and hot regions.
Power conversion technology: improving heat-transfer performance for low temperature fluid, developing plant design with high efficiency and low parasitic losses. It will increase the available resource basis to the huge low-temperature regions, not only those having favorable geological conditions.

## Slide 27
Operation technology: increasing production flow rate by targeting specific zones for stimulation, improving heat-removal efficiency in fractured rock system. Refine stimulation methods (permeability enhancement) for Engineered Geothermal Systems (EGS) and reduce the risk associated with induced seismicity. It will lead to an immediate cost reduction increasing the output per well and extending reservoir operating life.
Unconventional Geothermal Systems (UGR) technology: emerging activities to harness energy from nowadays non-economic reservoir would make significant progress with qualified input from research. in particular, reservoirs with supercritical fluids (fluids in the thermodynamic area above the critical temperature and pressure) and geopressurized reservoirs (deep sedimentary basins where fluids show high pressure and are rich of chemical elements or gases). This includes, beside peculiar power conversion and reservoir technology, also Operation & Maintenance techniques in aggressive geothermal environments, since they require specific solutions for corrosion and scaling problems. It will lead to an overall increase in power production
Geothermal Electricity: new technology
and research efforts

## Slide 28
Management technology: retrieve, simulate and monitor geothermally relevant reservoir parameters that influence the potential performance and long-term behavior. It includes the development of a Zero-emission technology, by mean of the total reinjection of fluid (and gases) within the reservoir without cooling and secondary effects It will secure the sustainable production achieved by using the correct production rates, taking into account the local resource characteristics (field size, natural recharge rate, etc.), extending the reservoir operating life and producing a benefit for the environment.
Geothermal Electricity: new technology
and research efforts

## Slide 29: JOINT PROGRAMME on GEOTHERMAL ENERGY
The goal of the JPGE is to contribute to the achievement of the SET Plan objectives, streamlining and coordinating national R&D programmes, accelerating the targeted development and maturing of next generation geothermal technology in order to provide industry with all the elements required for its large-scale and cost-effective deployment.
This target can be reached only through the application of new cost-effective technologies able to enhance the production of the already identified resources, to discover new untapped hydrothermal systems and to develop non hydrothermal systems.

## Slide 30
The GEISER (Geothermal Engineering Integrating Mitigation of Induced Seismicity in Reservoirs) project started at the beginning of the year 2010, with a funding of € 5.3 Mio granted for 3.5 years
Goal: to develop strategies to fulfil the task of the stimulation and improve the hydraulic properties of the geothermal reservoir without producing large earthquakes that pose a threat to buildings and disturb the public.
International Projects
Analysis of induced seismicity
Understanding the geomechanics and processes involved in induced seismicity
Consequences of induced seismicity
Strategies for the mitigation of induced seismicity

## Slide 32
Minimum LCOE nel 2030 in €/MWe

## Slide 33
For the classification of non-hazardous and hazardous waste, reference is made to EU legislation.
NON-HAZARDOUS SPECIAL WASTE
Debris from geothermal drilling
HAZARDOUS SPECIAL WASTE
Sludge produced by the condensation of geothermal steam
Residues of materials contaminated by geothermal fluids
Mitigation  DISPOSAL OR RECOVERY
SPECIAL WASTE

## Slide 34
Noise is mainly related to 3 phases:
DRILLING
CONSTRUCTION
TURBINES, COMPRESSORS, COOLING TOWERS
Under normal conditions, the production plant is very quiet.
MITIGATION
During drilling, a temporary protective shield can be constructed around the drilling platform and some machinery.
The buildings containing the generators and turbines are generally designed to ensure acoustic and thermal insulation, using soundproof walls.
NOISE POLLUTION