## Slide 1: UTES - Underground Thermal Energy Storage

## Slide 2: UTES - Underground Thermal Energy Storage: My research
Development of underground heat storage techniques through the treatment of geological and thermal data to define parameters significant to the suitability of the subsurface and natural and artificial materials to store heat while minimizing energy losses
Development of numerical models through the use of specific software (COMSOL Multiphysics & FEFLOW) to model the underground heat transport processes and then operate to laboratory testing and finally toward full-scale pilot testing

## Slide 3
The main objectives of the HeatStore project are:
to lower the cost
to reduce risks
to improve the performance of high temperature (~25°C to ~90°C) underground thermal energy storage (HT-UTES) technologies
to optimize heat network demand side management
There are 24 partners from 9 countries who are part of the Heatstore project. The consortium is composed of a mix of scientific research institutes and private companies. The industrial participation is considered a very strong and relevant advantage which is instrumental for success.

## Slide 4
The HEATSTORE project and this report comprise four different UTES systems:
High Temperature Aquifer Thermal Energy Storage (HT-ATES)
Borehole Thermal Energy Storage (BTES)
Pit Thermal Energy Storage (PTES)
Mine Thermal Energy Storage (MTES)

## Slide 5: High Temperature Aquifer Thermal Energy Storage (HT-ATES)
Figure 1. Principles of seasonal heat storage by the use of ATES in district heating (Heatstore)
ATES can take place by injection and later re-production of hot water in aquifers in both shallow and deep geological formations.
The geological conditions is the key prerequisite for establishing a HT-ATES system: the aquifers can be both unconsolidated sand units, porous rocks like sandstones or limestone or e.g. fractured rock formations).
The advantages of ATES systems include very large storage potential, low operational costs and high-term profitability.

## Slide 6: High Temperature Aquifer Thermal Energy Storage (HT-ATES)
A first positive outcome of the initial screening of the geological conditions will results in parameters characterisation like:
Geological and hydrogeological parameters
Hydrological (groundwater) properties
Geochemical properties for the groundwater
Thermal properties
For deep geothermal systems the following reservoir properties are also relevant:
Mineral composition of reservoir rock
Density of reservoir rock
Pressure in deep reservoirs
Compressibility

## Slide 7: High Temperature Aquifer Thermal Energy Storage (HT-ATES)
Operational scheme for ATES:
Pre-investigation (feasibility study)
Construction (Drilling, Design, Materials)
System integration
Operations feedback (Monitoring, Maintenance, Water treatment)

## Slide 8: High Temperature Aquifer Thermal Energy Storage (HT-ATES)
Case example - The German Reichstag (Berlin)
The underground storage is operational since 1999, however, the full capacity of the total system was reached in 2003.
Two aquifers at different depths are used to store cold (c. 60 m) and heat (c. 300 m).
The design temperature at the warm well is 70°C while charging (the storage temperature is limited to 70ºC because of geochemical aspects).
Figure 2. Illustration of HT-ATES system at the German Reichstag, Berlin (Sanner, B., Kabus, F., Seibt P. & Bartels, J. 2005)

## Slide 9: Borehole Thermal Energy Storage (BTES)
Figure 3. Layout of a borehole thermal energy storage and cross-section of a single borehole and u-tube (Sibbitt B. & McClenahan D., 2015)
BTES uses the natural heat capacity in a large volume of underground soil or rock to store thermal energy.
The principle is to heat up the subsurface and cool it down again by circulating a fluid in plastic u-tube pipes installed in a large number of closely spaced boreholes and completed with a sealing grout.
The distance between the boreholes is typically in the range of 2-5 m (boreholes of approx. 20-200 m depth).
Temperatures up to approx. 90°C can be stored and BTES can be used to store excess heat from industries, incineration plants and heat from renewable energy sources.

## Slide 10: Borehole Thermal Energy Storage (BTES)
A preliminary screening of the local geology in the area of the planned storage is mandatory and the required preliminary geological paramaters of the site are:
Geology
Groundwater flow (significant groundwater flow will cause advective heat loss and should be avoided)
Thermal properties (the higher the heat capacity the better)
The existing geological information will also typically provide important information in order to select the best drilling and grouting technique for the specific site (Sørensen, Per Alex. 2019)

## Slide 11: Borehole Thermal Energy Storage (BTES)
The project of Drake Landing Solar Community (Alberta, Canada) started in 2006 and was the first of this kind in North America. It provides heat for a group of 52 high energy-efficiency houses through an integrated system combining solar panels and a BTES.
The BTES system is composed of 144 boreholes with a depth of 35 meters and grouped in 24 parallel circuits.
Figure 4. Aerial view of the Drake Landing BTES (Sibbitt B. & McClenahan D., 2015)
Figure 5. Diagram of the system (Verstraete A. 2013)

## Slide 12: Pit Thermal Energy Storage (PTES)
PTES works by storing hot water in very large excavated basins with an insulated lid
Sides and bottom are typically covered by a polymer-liner (or concrete)
Temperatures up to approx. 90°C can be stored
Figure 6. Picture of Dronninglund Pit Storage under construction. Dronninglund District heating; 37,573 m2 of solar collectors and a 62,000 m3 water in pit heat storage (PlanEnergi)

## Slide 13: Pit Thermal Energy Storage (PTES)
Advantages:
Possibility for quick charging or discharging, short heat storage periods and the fact that water is ideal as storage medium due to high thermal capacity
Inherent stratification in the water column introduce storage water in different temperature intervals
If the ground conditions are optimal, the construction costs are low
Disadvantages:
The system is space demanding (the storage requires large areas without infrastructure, which makes it less feasible in urban areas)
The lifetime of liners and the lid construction is still partly unknown
High groundwater levels and poor soil conditions directly affects the construction costs

## Slide 14: Mine Thermal Energy Storage (MTES)
Figure 7. Location of the coal mine Markgraf II below the GZB well site (GZB) (Heatstore)
Mine water of abandoned and flooded mines is used as a low-temperature energy source for heating buildings (few plants exist in Germany and the Netherlands)
A pilot plant has not been established yet
The conceptual idea is based on storage of seasonal unutilized surplus heat during the summer from solar thermal collectors within the mine layout and to use the stored heat during the winter for heating purposes of buildings

## Slide 16: Main features of an energy storage system
Capacity: defines the energy stored in the system and depends on the storage process, the medium, and the size of the system
Power: defines how fast the energy stored in the system can be discharged (and charged)
Efficiency: is the ratio of the energy provided to the user to the energy needed to charge the storage system
Storage period: defines how long the energy is stored and lasts hours to months
Charge and discharge time: defines how much time is needed to charge/discharge the system
Cost: refers to either capacity or power of the storage system (depends on the costs of the storage equipment and its lifetime)

## Slide 17: Sensible Heat Storage (SHS)
SHS is the simplest method based on storing thermal energy by heating or cooling a liquid or solid storage medium (e.g., water, sand, molten salts, or rocks), with water being the cheapest option
The most popular and commercial heat storage medium is water, which has a number of residential and industrial applications
Underground storage of sensible heat in both liquid and solid media is also used for typically large-scale applications
SHS has two main advantages: it is cheap and without the risks associated with the use of toxic materials
SHS can be presented as Water Tank Storage, Underground storage (Aquifer storage, Cavern storage and Pit storage), Packed-bed storage

## Slide 18: Latent-Heat or Phase-Change Storage
LHS materials are known as PCMs due to their property of releasing or absorbing energy with a change in physical state
The energy storage density increases and hence the volume is reduced, in the case of LHS; the heat is mainly stored in the phase-change process at quite constant temperature
The use of an LHS system using PCMs is an effective way of storing thermal energy and has the advantages of high-energy storage density and the isothermal nature of the storage process (the main advantage over SHS)
Initially, these materials act like SHS materials in that the temperature rises linearly with the system enthalpy; however, later, heat is absorbed or release at almost constant temperature with a change in physical state

## Slide 19: SHS vs LHS
Figure 8. Methods of thermal energy storage: (a) sensible heat; (b) latent heat (I. Sarbu and C. Sebarchievici, 2018)

## Slide 20: Characteristics Proprieties of PCMs
Thermo-physical properties (latent heat of transition and thermal conductivity should be high, and density and volume variations during phase-transition should be, respectively, high and low in order to minimize storage volume)
Kinetic and chemical properties (materials should have long-term chemical stability, compatibility with materials of construction, no toxicity, and no fire hazard)
Economic advantages (low cost and large-scale availability of the PCMs are also very important)

## Slide 21: Phase Change Materials
Figure 9. Classification of phase-change materials (PCMs)(I. Sarbu and C. Sebarchievici, 2018)

## Slide 23: A new experimental apparatus to investigate heat transfer processes for ground heat exchangers
Figure 10. The design of the experimental apparatus and its components (Scotton, 2022)
The device will be used to evaluate, under controlled conditions, the temporal and spatial evolution of energy processes occurring between a thermal probe and the surrounding terrain.
The experimental apparatus is made of aluminium with dimensions around 2 m high, 1.5 m long and 1.1 m wide. The weight of the supporting structure is 200 kg, while the weight of the experimental apparatus in test configuration is 3000 kg.

## Slide 24: A new experimental apparatus to investigate heat transfer processes for ground heat exchangers
The device comprises perforated stainless steel walls, transparent PVC side walls, a fluid-distribution system and filtration fluid outlet tanks
Is equipped with a copper heat exchanger
Its purpose is to conduct controlled tests with filtration fluid and granular material (in this case a sandy-gravel material known as Risetta del Brenta)
There are two hydraulic circuits in the physical apparatus: the cold fluid circuit and the hot fluid circuit (the only functioning one at the moment). Both circuits can be connected to the thermal probe circuit or the filter fluid circuit.

## Slide 25: A new experimental apparatus to investigate heat transfer processes for ground heat exchangers
Figure 11. Diagram of the structural part of the experimental apparatus and the connection points of the hydraulic circuits of the geothermal probe and filtration fluid (Scotton, 2022)
The thermal probe circuit introduces fluid into the upper end of the copper probe and recovers it at the lower end of the probe
The filtration fluid circuit introduces the fluid to the bottom of the loading tank (inputCF) and the stability of filtration through the porous medium is ensured by two bypass channels located in the loading and unloading tank (output CF1 and outputCF2)
Both circuits are designed to maintain a constant flow rate with a constant temperature at the model inputs

## Slide 26: FEFLOW (Finite Element subsurface Flow system)
Figure 12. Feflow’s borehole heat exchanger setting menu (DHI-WASY Software FEFLOW – White Papers Vol V)

## Slide 27: Thank you for the attention!